## Slide 1: Usos y Costumbres del HoloLens
Sebastian Gambolati
Developer Sr.
Southworks

## Slide 2: Workshop agenda
HoloLens presentation
Inside HoloLens
How to Develop
Exercise 1 – HoloWorld
Exercise 2 – Inputs
Exercise 3 – Spatial Mapping / Sound
Exercise 4 – Vuforia / Cognitive Services integration

## Slide 3: HoloLens Presentation
DemoLens

## Slide 4: HoloLens Presentation
DemoLens

## Slide 5: Real Reality
Virtual Reality
Augmented Reality
Mixed Reality
HTC Vive
Oculus Rift
Google Tango
AR Kit
HoloLens
Acer
HP

## Slide 6: Prices comparison
Oculus Rift
U$D 598
HTC Vive
U$D 799
Google Tango: Lenovo Phab 2 Pro
U$D 500
ARKit: iPhone 7
U$D 769
Hololens
U$D 3000
Acer Mixed Reality Headset
U$D 299
HP Mixed Reality Headset
U$D 329

## Slide 7: Inside HoloLens
Optics
HoloLens has see-through holographic lenses
See-through holographic lenses (waveguides)
2 HD 16:9 light engines
Automatic pupillary distance calibration
Holographic Resolution: 2.3M total light points
Holographic Density: >2.5k radians (light points per radian)
Sensors
HoloLens has sensors for environment understanding and human understanding
1 IMU
4 environment understanding cameras
1 depth camera
1 2MP photo / HD video camera
Mixed reality capture
4 microphones
1 ambient light sensor

## Slide 8: Inside HoloLens (II)
Input / Output / Connectivity
Built-in speakers
Audio 3.5mm jack
Volume up/down
Brightness up/down
Power button
Battery status LEDs
Wi-Fi 802.11ac
Micro USB 2.0
Bluetooth 4.1 LE
Processors
The motherboard for Microsoft HoloLens
Intel 32 bit architecture with TPM 2.0 support
Custom-built Microsoft Holographic Processing Unit (HPU 1.0)

## Slide 9: Inside HoloLens (III)
Power
Battery Life
  2-3 hours of active use
  Up to 2 weeks of standby time
  Fully functional when charging
Passively cooled (no fans)
Memory
64GB Flash
2GB RAM
Weight
  579g

## Slide 10: How to Develop an HoloLens App
The MS way
Unity3D
HoloToolKit
Visual Studio 2015 (update 3) / 2017
HoloLens Emulator / HoloLens Device
Alternatives
UrhoSharp (by Xamarin)
Visual Studio + DirectX11

## Slide 11: EXERCISES
Exercise 1: HoloWorld
Exercise 2: Input
Exercise 3: Spatials
Exercise 4.1: Vuforia
Exercise 4.2: Cognitive Services
https://github.com/sGambolati/HoloWorkShop
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 12: Exercise 1: HoloWorld
Briefing:
  You will get your first Holographic App with a basic hologram.
Goals:
  Get familiar with Unity3D.
    GameObjects
    Component
    Prefab
    Assets
  Import HoloToolKit.
  Generate Visual Studio project.
  Deploy to HoloLens Device / Emulator.

## Slide 13: Exercise 2: Input
Briefing:
  You will get your hologram reaction to user interactions.
Goals:
  Place a Gaze.
  Handle User Air Tap.
  Handle User Air Tap & Hold.
  Handle Voice Action Input.
  Play Text to Speech.

## Slide 14: Exercise 3: Spatial Mapping / Sound
Briefing:
  Your application will interact with the user environment.
Goals:
  Map user room.
  Query place where to place hologram into real world.
  Add spatial sound to holograms.
  Learn about UI elements
    HeadIndicator
    TagAlong
    Billboard

## Slide 15: Exercise 4: Vuforia / Cognitive Services Integration
Briefing:
  Your application will use third party service to extend its behavior.
Goals:
  Image recognition with Vuforia.
  Object recognition with Vuforia.
  Face recognition with Cognitive Services’ FaceAPI.
  Query user context with Cognitive Services’ Computer Vision.

## Slide 16: Thanks for your code!
http://dotgblog.wordpress.com
@sggambolati
sebastian.gambolati@southworks.com
Sebastian Gambolati